## Slide 1: MES Project Volume control using an ultrasonic sensor
Author: Andronic Smaranda
Master’s Program: ACES

## Slide 2: PROJECT DESCRIPTION
This project aims to understand low-level programming on an ARM-based STM32 microcontroller by working directly with registers, timers, GPIOs, and interrupts.
As a practical example, an ultrasonic alarm system was implemented using an HC-SR04 sensor and a buzzer, where the alarm behaviour changes based on the detected distance.

## Slide 3: Hardware setup
Components used:
Microcontroller: STM32L476 Nucleo development board
Ultrasonic distance sensor: HC-SR04
Buzzer : Piezoelectric active buzzer

## Slide 4
Piezoelectric buzzer
Ultrasonic sensor
STM32L476 Nucleo development board

## Slide 5: Software Pipeline
Timer interrupts are triggered by hardware events on the ultrasonic sensor’s echo pin and are used to capture precise timing information without blocking the main program flow.

## Slide 6
Custom functions.
Not using HAL for configuring timers
The echo pin is connected to TIM1 in input capture mode, which generates interrupts on both the rising and falling edges of the echo signal
Sensor_Trigger() sends a precise 10 µs trigger pulse to the ultrasonic sensor, resets the timer, and prepares the system to measure the echo pulse using timer interrupts.
This function configures Timer 3 (TIM3) at register level to generate a PWM signal used to drive the active buzzer on PA6 (TIM3_CH1).